## Slide 1
FYI26 · AIRBUS FLY YOUR IDEAS 2026
AI Guardian
Human-in-the-Loop Anomaly Detection for Connected Aerospace Systems
Kedia Ihogoza · Project Manager / AI-ML / SCM
David Roset · Database / Dashboard / QA
Stage 5 — Project Closure | MVP Demonstration

## Slide 2
THE PROBLEM & OUR MVP
Catching failures before the operator does
Connected aircraft stream continuous telemetry between sensors, autopilots and ground operators. That visibility also opens new, potentially catastrophic failure modes that are easy to miss in a live feed.
THE GUARDIAN SITS BETWEEN RAW TELEMETRY AND THE HUMAN
Every detection is explained.
Every alert includes a recommended action.
Every decision stays with the operator.
KEY FAILURE MODES WE DETECT
Packet loss / reorder
Loss of situational awareness
GPS spoof or jump
Navigation error, collision
IMU dropout / frozen data
Wrong attitude estimation
Battery degradation
Unexpected power loss
GPS / IMU inconsistency
Sensor-fusion breakdown

## Slide 3
HOW WE GOT HERE
From idea to functional MVP in five stages
1
Ideation
Team formation, problem framing, MVP concept for aerospace safety.
2
Planning
Project charter, scope, roles, sprint roadmap and risk plan.
3
Tech Docs
Architecture, DB schema, API + telemetry contracts, tech stack.
4
Development
3 Agile sprints — engine, ML, dashboard, live ingestion, deploy.
5
Closure
This review: results, lessons learned, demo & retrospective.
Agile throughout: tasks broken into small units, assigned explicitly, and tested after every change.

## Slide 4
TECHNICAL SHOWCASE
Architecture, engine & data design
Telemetry Sources
CSV replay · UDP · Serial · MAVLink (ArduPilot / PX4)
▼
Guardian Engine
10 deterministic rules + Isolation Forest ML → build_alert()
▼
Persistence
SQLite (WAL) store + JSONL export of every alert
▼
Flask + React Dashboard
Live telemetry, alert feed, ACK / Escalate / Resolve
WHY THESE CHOICES
Rules + ML together
Rules give explainable, deterministic catches; Isolation Forest catches the unknown.
SQLite (WAL)
Zero-config, concurrent reads for the live dashboard, portable single-file DB.
Flask + React
Lightweight REST backend; typed React/Leaflet UI for live map + alerts.
MAVLink / pymavlink
Speaks the real autopilot protocol — works with ArduPilot & PX4.

## Slide 5
LIVE DEMO
Five features we'll walk through
Geofencing
Real-time no-fly-zone breach detection with severity + reason.
Post-Flight AI Report
Claude-generated, plain-language safety summary per flight.
Predictive Alerts
Forecasts battery depletion & IMU drift before failure.
Auth & RBAC
Hashed passwords, admin vs. user roles, session-guarded dashboard.
Public Landing Page
Project front door explaining the Guardian to visitors.
Operator Actions
ACK / Escalate / Resolve every alert — human stays in the loop.
Demo path: MAVLink / SITL feed → engine flags anomaly → alert appears on dashboard → operator acknowledges.

## Slide 6
RESULTS
The MVP works — and we can measure it
162
TESTS PASSING
86.4%
PRECISION
90.9%
RECALL
11/11
SCENARIOS PASSED
Chart: Detection quality & delivery (%)
| Precision | Recall | Scenario pass | Feature delivery
Score | 86.4 | 90.9 | 100 | 100
VS. THE PROJECT CHARTER
All 5 planned MVP features delivered.
Real-time detection on live MAVLink feed.
Recall > precision by design — miss fewer real hazards.
Containerized deploy + CI on GitHub Actions.

## Slide 7
LESSONS LEARNED
What the project taught us
WHAT WENT WELL
Explainability first
Pairing rules with ML kept every alert traceable — critical for aerospace trust.
Clear task ownership
Explicit role split (PM/ML vs. DB/QA) reduced blocking and merge conflicts.
Test after every change
162 tests caught regressions early and made the demo dependable.
WHAT WE'D IMPROVE
Budget more for integration
Wiring MAVLink to the live dashboard took longer than estimated.
Earlier QA on ML thresholds
Tuning precision/recall late cost time; bake it in from sprint 1.
Tighten commit hygiene
A few stray files reached main — enforce PR checks next time.
Thank you — questions welcome. | github.com/Kedia12/fyi26-ai-guardian